Notes for the CFV Safety Speaker

NPRM/Final Rule Focus

NPRM / Final Rule Purpose:

To implement direct and non-discretionary parts of 2010/2012 Auth Acts (CGAA & CGMTA).

- Subpart C applicability is now 3 NM vs Boundary Line

- Out-of-water survival craft if ops beyond 3 NM

- Record of equipment maintenance and drills

- Dockside safety exams

- Survey and classification;  Load lines

- Medical supplies, navigation equipment, marine radios, Ground tackle

Vessel parity. Some statutory provisions with respect to special equipment requirements apply only to the subset of CFVs that operate beyond U.S. Boundary Lines (which, as subsequently discussed, the CGAA changed to beyond three (3) nautical miles from the U.S. territorial sea baseline), or with more than 16 persons onboard, or that are Aleutian Trade fish tender vessels. These CFVs, so identified, are subject to special Coast Guard regulatory requirements that are set forth in 46 CFR part 28, subpart C, and referred to throughout the rule preambles as “subpart C CFVs”.  Until enactment of the CGAA, only federally documented CFVs were required to comply with the special equipment requirements;   the (typically) smaller CFVs, that require only State registration, were excluded. The CGAA required uniform safety standards and equipment requirements for all CFVs (whether documented or undocumented) that operate beyond three (3) nautical miles of the baseline of the territorial sea or the coastline of the Great Lakes. This rule proposes to implement the CGAA by revising subpart C to reflect that change in applicability.

Some existing subpart C regulatory requirements are the result of prior Coast Guard discretionary determinations that the requirement is necessary for the safety of the documented CFVs to which subpart C formerly was restricted. The Coast Guard declines to extend those same requirements to undocumented CFVs because the proposed rule focuses exclusively on CGAA and CGMTA mandates, and the Coast Guard is not using any discretionary authority, which would be required in order to make such a determination. The proposed rule would amend subpart C to clarify that, at least for now, the proposed changes would apply only to documented subpart C CFVs.

Substitution of baseline for Boundary Line criteria. Special statutory provisions involving safety standards apply to the subset of CFVs that operate relatively far from shore, or with more than 16 persons onboard, or that are Aleutian Trade fish tender vessels. Formerly, the relevant distance from shore was defined as “beyond the Boundary Line.” The location of the Boundary Line is set by Coast Guard regulation and varies by distance from the coastline around the country. The CGAA redefined the relevant distance as “beyond 3 nautical miles from the baseline from which the territorial sea of the United States is measured or beyond 3 nautical miles from the coastline of the Great Lakes,” and this rule proposes to align regulatory language accordingly.

Survival craft. Until the CGAA was enacted, certain CFVs were allowed by statute and regulation to use life floats or rigid buoyant apparatus as survival craft. The CGAA requires survival craft, on all CFVs, to fully protect the occupants from exposing any part of the body to immersion in water.  This rule proposes to include that requirement in the CFV regulations.

Records. This rule proposes to amend the CFV regulations so that they include the CGAA requirement that individuals in charge of certain CFVs keep records of equipment maintenance, and crew instruction and drills.

Vessel examinations. Until the CGAA was enacted, the only CFVs required by the Coast Guard to undergo dockside safety examinations were fish processors, or fish tenders in the Aleutian trade. This rule proposes to incorporate the CGAA and CGMTA provisions that extend dockside examination requirements to any subpart C CFV. Dockside examinations must take place at least once every 5 years, with the first examinations to have been completed by October 15, 2015.

Construction standards for smaller vessels. This rule proposes to amend CFV regulations to include the CGAA requirement for CFVs under 50 feet in length and built in 2010 or later to comply with Coast Guard construction standards for recreational vessels.

Load lines. Until the CGAA was enacted, CFVs were exempt from all statutory or regulatory load line requirements. This rule proposes to amend Coast Guard regulations to reflect the CGAA and CGMTA provisions that remove the load line exemption for CFVs built after July 1, 2013.

Classing of vessels. Until the CGAA was enacted, a fish processor had to meet all survey and classification requirements prescribed by the American Bureau of Shipping or another organization approved by the Coast Guard, if it was built or converted after July 27, 1990. The CGAA and the CGMTA extended this requirement to any subpart C CFV of 50 feet or more overall in length and built after July 1, 2013.  This rule proposes to amend Coast Guard regulations to incorporate the 2010 and 2012 vessel classing requirements.

Termination of unsafe operations. This rule proposes to amend Coast Guard regulations so they reflect the broader CGAA authority to terminate a CFV's operations if the Coast Guard observes it operating under unsafe conditions, or if the CFV lacks required documentation like a certificate of having passed a dockside examination.

Miscellaneous equipment. This rule proposes to amend Coast Guard regulations for subpart C vessels to include CGAA requirements for marine radios, navigation equipment, medical supplies, and ground tackle.